## Slide 1: Anglicky v odborných předmětech "Support of teaching technical subjects in English“
Tutorial: Mechanic – electrician
Topic: Electronics
II. class
RC Filters:
RC High Pass Filter
Prepared by: Ing. Jaroslav Bernkopf
AVOP-ELEKTRO-Ber-008
Projekt Anglicky v odborných předmětech, CZ.1.07/1.3.09/04.0002
je spolufinancován Evropským sociálním fondem a státním rozpočtem České republiky.

## Slide 2: Definition
A high-pass filter is a circuit that passes high-frequency signals but attenuates signals with frequencies lower than the cutoff frequency.
-3 dB
Passband
Stopband
Slope:
20 dB/decade
(6 dB/octave)
Cutoff frequency
f

## Slide 3: Description
The simplest high-pass filter consists of one resistor and one capacitor.
We call it the RC high-pass filter.
Stopband
Passband
-3 dB
Cutoff frequency
f
A
Slope:
20 dB/decade
(6 dB/octave)

## Slide 4: Description
f
0
1
Av
Let‘s construct the gain-frequency characteristic of the RC high-pass filter.
Let‘s apply a voltage Vin of a very low frequency to the input of the circuit.
If the frequency becomes lower and lower, the input voltage will become a DC voltage.
No DC current can pass through the capacitor because there is an insulator between its electrodes.
No DC signal can pass from the input of this circuit to its output.

## Slide 5: Description
f
0
1
At zero frequency the output voltage Vout will be zero:
=
The voltage gain Av is
Av = 0
Av
f = 0

## Slide 6: Description
We have the first point of the gain-frequency characteristic:
At zero frequency the voltage gain Av is equal to zero.
f
0
1
Av = 0
Av
f = 0

## Slide 7: Description
Let‘s apply a voltage Vin of a very high frequency and of an amplitude of 10V to the input of the circuit.
At a very high frequency the capacitor represents a short circuit – similar to a wire link.
If the output pin is shorted with the input pin, there must be the same signal on it.
f
0
1
Av

## Slide 8: Description
The output voltage Vout is the same as the input voltage Vin = 10 V.
Therefore
=
The voltage gain Av is
We have the second point of the gain-frequency characteristic:
At infinite frequency the voltage gain Av is equal to unity.
f
0
1
Av
f = ∞
Av = 1

## Slide 9: Description
Between these two points there is a point where the gain stops rising and starts to be unity.
We call this point the cutoff frequency.
f
0
1
Av
fc
Gain is rising
Gain is unity
Av = 0,707

## Slide 10: Description
In the passband all signal passes from the input to the output.
The voltage gain Av is equal to unity.
Stopband
Passband
-3 dB
Cutoff frequency
f
A
Slope:
20 dB/decade
(6 dB/octave)

## Slide 11: Description
Stopband
Passband
-3 dB
Cutoff frequency
f
A
Slope:
20 dB/decade
(6 dB/octave)
In the stopband the lower the frequency, the lower the voltage gain Av.
The gain Av falls off at 20 dB per decade (or 6 dB per octave, which tells the same).
When the frequency decreases by a factor of 10, the gain decreases by a factor of 10 (i.e. 20 dB).
When the frequency decreases by a factor of 2, the gain decreases by a factor of 2 (i.e. 6 dB).

## Slide 12: Description
At the cutoff frequency fc the voltage gain Av falls to .
In other words the gain is reduced by 3 dB.
Here is the formula for the cut-off frequency:
Stopband
Passband
-3 dB
Cutoff frequency
f
A
Slope:
20 dB/decade
(6 dB/octave)

## Slide 13: High pass filter– video
  Passive RC high pass filters
  https://www.youtube.com/watch?v=4CcIFycCnxU

## Slide 14: High pass filter– video
  Passive RC low and high pass filter
  https://www.youtube.com/watch?v=lagfhNjMuQM

## Slide 15: Task
Calculate the cut-off frequency for the circuit below and state if it is a high pass or low pass filter.
10k
10n

## Slide 16: Solution
10k
10n
The cut-off frequency of the circuit is 1 592 Hz.
A signal of the lowest frequency – a DC signal – can‘t pass through the capacitor because there is an insulator between its electrodes.
A signal of a high frequency passes without attenuation because the capacitor represents a short circuit.
The circuit is a high-pass filter.

## Slide 17: References
http://www.wikipedia.com
http://www.thefreedictionary.com
http://www.animations.physics.unsw.edu.au/jw/calculus.htm
http://openlearn.open.ac.uk/