## Slide 1: Anglicky v odborných předmětech "Support of teaching technical subjects in English“
Tutorial: Mechanic -electrician
Topic: Electronics
II. class
Transistors:
Transistor CE Amplifier
Prepared by: Ing. Jaroslav Bernkopf
AVOP-ELEKTRO-Ber-009
Projekt Anglicky v odborných předmětech, CZ.1.07/1.3.09/04.0002
je spolufinancován Evropským sociálním fondem a státním rozpočtem České republiky.

## Slide 2: Definition
A transistor common emitter amplifier is a circuit where the input signal is applied between the base and the emitter while the output is taken from between the collector and the emitter.
The emitter is grounded and is common to both the input and output.
Hence the name: Common emitter amplifier.

## Slide 3: Description
When analyzing and designing the circuits we will use the following formulas:
Where
IC = current flowing into the collector
IB = current flowing into the base
IE = current flowing out of the emitter
VBE = voltage across the base–emitter diode
VB = base voltage with respect to ground
(beta) = current gain of the transistor. It is the same as h21e or hFE.
means „approximately equal“.

## Slide 4: Description
When we apply a positive voltage to the base, a current IB flows into the base.
A ß (beta) times higher current IC flows through the RC into the collector.
A small change of the base current IB makes a ß times bigger change of the collector current IC:

## Slide 5: Description
The collector current IC creates a voltage drop VRC across the collector resistor RC.
The higher the base voltage, the bigger the voltage drop VRC, and the lower the collector voltage Vout.
An increase in base input voltage Vin causes a decrease in collector output voltage Vout.
This is why we call this circuit an "Inverting Amplifier“.
A small change of the base voltage makes a big change of the collector voltage.
The input signal applied on the base appears, amplified, on the collector.
VRC
VCC
Vout

## Slide 6: Task
All bias components have been omitted to simplify the above explanations.
In the next task, we will design a real amplifier stage including the setting and stabilization of the operating point.
The operating point of a transistor, also known as bias point, quiescent point, or Q-point, is the steady-state operating condition of a transistor with no input signal applied.
(Wikipedia)
RE

## Slide 7: Task
Given the following conditions, calculate the values of all resistors for the circuit below.
IC = 1 mA
VCE = 5 V
VE = 2 V
ß ≥ 100
Current IR1R2 through the voltage divider R1, R2 about 10 times the max IB
IC=1mA
IR1R2
VE=2V
VCE=5V
RE

## Slide 8: Solution
IC=1mA
IR1R2
RE
IE=1mA
2k
VE=2V
VCE=5V

## Slide 9: Solution
IR1R2 = 10* IB = 10*0.01mA = 0.1mA
VB = VR2 = VE + VBE = 2V + 0.7V = 2.7V
IC=1mA
IR1R2
RE
IE=1mA
VB = VR2 = 2.7 V
2k
27k
VE=2V
VCE=5V

## Slide 10: Solution
IC=1mA
IR1R2
RE
IE=1mA
VB = VR2 = 2.7 V
2k
VR1 = VCC – VR2 = 12V – 2.7V = 9.3V
27k
VR1 = 9.3 V
93k
VE=2V
VCE=5V

## Slide 11: Solution
IC=1mA
IR1R2
VE=2V
VCE=5V
RE
IE=1mA
VB = VR2 = 2.7 V
2k
27k
VR1 = 9.3 V
93k
5k
VRC=5V
VCC=12V

## Slide 12: Solution
IC=1mA
IR1R2
VE=2V
VCE=5V
RE
IE=1mA
VB = VR2 = 2.7 V
2k
27k
VR1 = 9.3 V
93k
5k
VRC=5V
VCC=12V
When solving the task we have only needed three simple rules:
Ohm‘s law
Kirchhoff‘s voltage law
Kirchhoff‘s current law

## Slide 13: Solution
IC=1mA
IR1R2
VE=2V
VCE=5V
RE
IE=1mA
VB = VR2 = 2.7 V
2k
27k
VR1 = 9.3 V
93k
5k
VRC=5V
VCC=12V
Ohm‘s law:

## Slide 14: Solution
IC=1mA
IR1R2
VE=2V
VCE=5V
RE
IE=1mA
VB = VR2 = 2.7 V
2k
27k
VR1 = 9.3 V
93k
5k
VRC=5V
VCC=12V
Kirchhoff‘s voltage law:

## Slide 15: Solution
IC=1mA
IR1R2
VE=2V
VCE=5V
RE
IE=1mA
VB = VR2 = 2.7 V
2k
27k
VR1 = 9.3 V
93k
5k
VRC=5V
VCC=12V
Kirchhoff‘s current law:

## Slide 16: References
http://en.wikipedia.org/wiki/Common_emitter
http://www.thefreedictionary.com
http://www.animations.physics.unsw.edu.au/jw/calculus.htm
http://openlearn.open.ac.uk/
http://www.dnatechindia.com/Tutorial/Transistors/Bipolar-Transistor.html
http://talkingelectronics.com/pay/TEI-Index-Full.html