## Slide 1: Anglicky v odborných předmětech "Support of teaching technical subjects in English“
Turorial: Mechanic – electrician
Topic: Electronics
II. class
Transistors:
Transistor CE Switch
Prepared by: Ing. Jaroslav Bernkopf
AVOP-ELEKTRO-Ber-010
Projekt Anglicky v odborných předmětech, CZ.1.07/1.3.09/04.0002
je spolufinancován Evropským sociálním fondem a státním rozpočtem České republiky.

## Slide 2: Definition
A transistor common emitter switch is a circuit where the input signal on the base switches on or off the current to the load, which is connected between the collector and the power supply.
A small base current controls a much larger collector load current.
The emitter is grounded.
... is equal to ...

## Slide 3: Description
When analyzing and designing the circuits we will use the following formulas:
Where
IC = current flowing into the collector
IB = current flowing into the base
VBE = voltage across the base–emitter diode
(beta) = current gain of the transistor. It is the same as h21e or hFE.

## Slide 4: Description
When there is no voltage and no current applied to the base, no current flows through the load.
The transistor is switched off.
Its resistance is infinite.
The load is disconnected.
The transistor in this state is equal to an open switch.
... is equal to ...

## Slide 5: Description
When we apply a positive voltage to the base, a current IB flows into the base.
A ß (beta) times higher current IC flows through the load into the collector.
A small change of the base current IB makes a ß times bigger change of the collector current IC:

## Slide 6: Description
The collector current IC creates a voltage drop VL across the load.
The higher the base current, the bigger the voltage drop VL, and the lower the collector voltage VC.
An increase in base current IB causes a decrease in collector voltage VC.
If we keep raising the base current IB, the collector voltage VC falls down to zero.
VL
VCC
VC

## Slide 7: Description
When there is an appropriate current applied to the base, full current flows through the load.
The transistor is switched on.
Its resistance is zero.
The load is directly connected to the VCC.
The transistor in this state is equal to a closed switch.
There is no voltage drop between the collector and the emitter.
... is equal to ...

## Slide 8: Task
Given the values of the components in the following picture, calculate the value of the resistor R1.
The voltage drop across the LED D1 is 2V.
VCC is equal to 5 V.
74ALS00

## Slide 9: Solution
To solve the circuit we will have to know / calculate:
current flowing through the LED and the transistor
current gain of the transistor
base current needed to switch the transistor on
voltage available on the output of the gate
74ALS00

## Slide 10: Solution
The current flowing through the LED and the transistor
The voltage drop across the transistor is (or should be) zero.
The voltage drop across the LED is 2V.
The voltage drop across R2 is
VR2 = 5V – 2V = 3V
The current through R2 and through the transistor is
IC=20mA
74ALS00

## Slide 11: Solution
The current gain of the transistor
The minimum current gain hFE for the transistor BC337-25 is 160.
hFE is the same as ß.
We will use the symbol ß.
IC=20mA

## Slide 12: Solution
The base current needed to switch the transistor on
That implies:
To be sure that the transistor will be really switched on we choose a twice higher IB, i.e. 0.25mA.
IC=20mA
IB=0.25mA
74ALS00

## Slide 13: Solution
The voltage available on the output of the gate
The minimum guaranteed voltage on the output of 74ALS00 is
The voltage drop VR1 across R1 is

## Slide 14: Solution
IC=20mA
IB=0.25mA
74ALS00
Using the Ohm‘s law we can now calculate the value of R1:
We choose the closest standard 5% resistor value: 9k1.
9k1

## Slide 15: References
http://en.wikipedia.org/wiki/Common_emitter
http://www.thefreedictionary.com
http://www.animations.physics.unsw.edu.au/jw/calculus.htm
http://openlearn.open.ac.uk/
http://www.dnatechindia.com/Tutorial/Transistors/Bipolar-Transistor.html
http://talkingelectronics.com/pay/TEI-Index-Full.html